## Slide 1: Report 06/14/2020 Tengteng Tao
Questions have been solved:
What is the charge carrier in CdTe? Is it p or n type?
What metallic contacts that one usually use for CdTe film?
If good contacts can be made on CdTe film of about 10 mm by 10 mm size, can this sample be mounted in the Hall effect measurement instrument? Any extension conducting wires needed?
Study what is vapor transport growth method.

## Slide 2: Report 06/14/2020 Tengteng Tao
Cadmium Telluride (CdTe) :
Cademium Telluirde(CdTe) is a stable crystalline compound formed from cadmium and tellurium. CdTe usually sandwitched with Cadmium Sulfide(CdS) to form a p-n junction. In this p-n junction, CdTe is p type. Accordingly, the majority charge carriers are holes and the minority charge carriers are electrons. However, CdTe layer deposited form an acidic electrolyte showed an n-type conduction. I think more specific conditions are needed to produce this n-type CdTe. I will do more research on this topic if needed.
Question:
In this question, you also mentioned intentional doping. I did not find out too much information on this topic, and I am curious about this topic. The CdTe has more holes than electrons, which decide that this material is p type in a p-n junction. How can we change this property and make it a n type in the junction?
The only way I found that can change the charge carrier of the CdTe is controlling the impurities of doping acceptor or donor. I also find out some concept like if we replace Cd with In, we can make a n-type material; if we replace Cd with Cu, Ag, and Au, we can form a p-type semiconductor. However, I did not find the specific way to achieve this.

## Slide 3: Report 06/14/2020 Tengteng Tao
Hall effect on Cadmium Telluride (CdTe) :
Based on my reading, for Al, Ag and Cu surfaces, CdTe has a weak chemisorption and large interfacial distances. Medium or strong chemisorption and small interfacial distances are found between CdTe and Au and Ni surfaces. The CdTe forms n-type Schottky contacts with Ag, Al and Cu and p=type Schottky contacts with Au and Ni at the interface between metalized CdTe and semi conductive CdTe.
Question:
I am not really understand the meaning of metallic contacts and did not find any definition about those contacts, but I still read some paper about the Hall effect on the CdTe film. One paper I have read has detailed descriptions about the experiment and setup, but I am not sure if those information are important or not . I think I need some further instruction in this part.

## Slide 4: Report 06/14/2020 Tengteng Tao
If good contacts can be made on CdTe film of about 10 mm by 10 mm size, can this sample be mounted in the Hall effect measurement instrument? Any extension conducting wires needed?
For this question, I think the size will be perfect for the Hall effect measurement instrument, because the tested sample I used before is about 10mm by 10mm size. Accordingly, once we have such a sample, we can mounted it in the instrument easily. However, I am not sure if we needed extension conduction wires or not. Typically, the machine just used VDP method and produce magnetic field and current to the sample. There is no special requirement for the testing sample. However, I did not really know the CdTe film, I think we need more information to solve this problem.
Study what is vapor transport growth method.
I have found some paper in this topic. Once I finished reading those paper, I will conclude the information I get and list the questions.